Investigation of DC circuits with series connected resistors. Investigation of DC circuits with parallel resistors.

1 Laboratory work

- What is considered to be series connected circuit?

- Formulate Ohm's law and the second Kirchhof law.

- How to relate the voltage added to the series-mounted receivers,  with a voltage of the each receiver?

- How will change the voltage in the resistor R2 if we change resistance of the resitor VR1?

- Parallel cirquit. Draw, explain how we can calculate various parameters.

- Formulate Ohm's law and the first Kirchhofs law.

- How will change current I4, if we increase resistance of resistor R5 two times?

- Calculate the current I, where U = 10 V, R4 = 30 Ω, R5 = 100 Ω, R6 = 200 Ω (parallel mounted).

- What is the power drawn from the power source, if the four receivers are connected in parallel, and their resistance, respectively equal to: R1 = 50 Ω, R2 = 100 Ω, R3 = 200 Ω, R4 = 50 Ω? Receivers connected to a 12V power source.

Investigation of series AC Circuit.

2 Laboratory work

- Explain in which cirquit and in what conditions we can see phenomena of voltage resonance?

- How we can determine ,from the readings of multimeters, that the cirquit is set to voltage resonance?

- How we can determine ,from the readings of multimeters, when φ> 0 and when φ <0?

- Draw the circuit diagram of vectors, where R ≠ 0, and XL> XC.

- Draw the circuit diagram of vectors, where R ≠ 0, and XL< XC.

- Explane the change of cos φ changing capacitance.

Investigation of single-phase transformer.

3 Laboratory work

- Explain the structure of the transformer , operation principle and purpose.

- What we call the transformation and efficiency coefficient?

- Why the transformation coefficient is calculated in the idle work mode?

- How we determine energy losses in the transformer?

- Explain how the efficiency η depends on the current strength of the secondary winding.

Investigation of logic elements.

4 Laboratory work

- Everything what you know about AND logic function.

- Everything what you know about OR logic function.

- Everything what you know about NO logic function

- What is the full set of the elemts.

- Having full element set OR-NON, construct logic function OR.

- Having full element set OR-NON, construct logic function AND.

- Having full element set OR-NON, construct logic function AND-NON.

- Having full element set AND-NON, construct logic function AND.

- Having full element set AND-NON, construct logic function OR.

- Having full element set AND-NON, construct logic function OR-NON.

Investigation of single-phase current rectifier.

5 Laboratory work

- Explain the operating principle of semiconductor diode.

- Explain the purpose of the test circuit elements.

- Draw one-sided and double-rectifier schemes and explain their operation.

- Draw and explain one-and two-way rectifier adjusted voltage curves U = f(t).

- What advantages and disadvantages are of the different rectifiers?

- How to define the filtration and pulsation rates?

- Explain the operating principle of the C filter.

- Explain the operating principle of the L filter.

- Explain when is better to use C filter and when – L filter?