Investigation of DC circuits with series connected resistors. Investigation of DC circuits with parallel resistors.

1 Laboratory work

- What is considered to be series connected circuit?

- Formulate Ohm's law and the second Kirchhof law.

- How to relate the voltage added to the series-mounted receivers,  with a voltage of the each receiver?

- How will change the voltage in the resistor R2 if we change resistance of the resitor VR1?

- Parallel cirquit. Draw, explain how we can calculate various parameters.

- Formulate Ohm's law and the first Kirchhofs law.

- How will change current I4, if we increase resistance of resistor R5 two times?

- Calculate the current I, where U = 10 V, R4 = 30 Ω, R5 = 100 Ω, R6 = 200 Ω.(parallel mounted).

- What is the power drawn from the power source, if the four receivers are connected in parallel, and their resistance, respectively equal to: R1 = 50 Ω, R2 = 100 Ω, R3 = 200 Ω, R4 = 50 Ω? Receivers connected to a 12V power source.

Investigation of series circuit AC Circuit.

2 Laboratory work

- Explain in which cirquit and in what conditions we can see phenomena of voltage resonance?

- How we can determine ,from the readings of multimeters, that the cirquit is set to voltage resonance?

- How we can determine ,from the readings of multimeters, when φ> 0 and when φ <0?

- Draw the circuit diagram of vectors, where R ≠ 0, and XL> XC.

- Draw the circuit diagram of vectors, where R ≠ 0, and XL< XC.

- Explane the change of cos φ changing capacitance.

Investigation of single-phase transformer.

3 Laboratory work

- Explain the structure of the transformer , operation principle and purpose.

- What we call the transformation and efficiency coefficient?

- Why the transformation coefficient is calculated in the idle work mode?

- How we determine energy losses in the transformer?

- Explain how the efficiency η depends on the current strength of the secondary winding.

Investigation of a three-phase, Y-connected circuit.

4 Laboratory work

- Explain the connection of Y circuit in the three-phase network.

- What kind of receiver is considered symmetrical?

- What kind of receiver is considered asymmetric?

- Can a three-phase network receiver work without a neutral wire?

- What happens if we cut neutral wire in three-phase network symmetrical receiver.

Investigation of a three-phase asynchronous motor and frequency converter.

5 Laboratory work

- How we can controll asynchronous motors rpm?

- How is the engine power is taken from the network?

- Explain how you can change the rotation direction of the motor.

- Explain how to make the three-phase asynchronous motor work one- phase network.